## Slide 1
AIORI HACKATHON 3 · PS-032
Path & Reachability
Analysis During RPKI
State Changes
TEAM DEBUGS
A precise, event-driven view of how routing validity changes propagate into reachability risk.

## Slide 2
AIORI HACKATHON 3
Meet Team Debugs
Three minds. One mission.
JASMEET
SAKEC
Team Lead
problem understanding and solution design
NISHANT
SAKEC
Data Engineer
analysis pipeline
UMA
SAKEC
Results Analyst
case studies, report
and demo

## Slide 3
Problem Description
RPKI state is not static. ROA additions, withdrawals, and edits can instantly change route validity — but operators still lack a fast explanation of which AS paths and destinations are newly exposed.
THE GAP
• Validation feeds show state, not impact
• Full recomputation is slow at Internet scale
• Invalid does not always mean unreachable
• Root cause is buried across time and topology
Required outcome
Given an RPKI state change, identify affected prefixes, changed paths, reachability consequences, and the evidence behind each result.

## Slide 4
Background
Three layers determine whether a route is trusted and usable.
RPKI / ROA
BGP / AS PATH
REACHABILITY
Cryptographic intent
Control-plane evidence
Operational consequence
ROAs authorize an origin AS for a prefix and maximum length.
BGP paths reveal observed origin and AS-level propagation.
Policy determines acceptance; topology determines alternatives.
Key distinction: ROV validity is a policy input — not a direct reachability verdict.

## Slide 5
Literature and RFC Review
[1] RFC 6480
Defines the RPKI architecture and trust model.
[2] RFC 6811 / 8893
Specifies origin validation and clarifies operational use.
[3] RFC 8205
BGPsec path validation: relevant context, distinct from ROV.
[4] RFC 8416
Operational guidance for route origin validation deployment.
Design implication
Keep cryptographic validity, observed path change, and inferred reachability as separate evidence layers.

## Slide 6
Proposed Solution
An incremental, evidence-preserving five-step pipeline
1 INGEST
RPKI + BGP
2 DIFF
State changes
3 SCOPE
Affected routes
4 ANALYZE
Paths + reachability
5 EXPLAIN
Ranked evidence
Normalize snapshots and event streams
Detect ROA add, withdraw, modify
Map prefixes, origins, paths and peers
Recompute only impacted graph regions
Emit severity, cause and trace
OUTPUT · affected prefix → changed validity → path delta → reachability confidence → evidence

## Slide 7
Optimization Proposed
Move from periodic global recomputation to targeted incremental analysis.
DIMENSION
BEFORE · NAIVE
AFTER · PROPOSED
Trigger
Periodic full scan
Event-driven state diff
Scope
All prefixes and paths
Impacted prefix / origin subgraph
Computation
Repeated graph rebuild
Cached indices + incremental update
Output
Validity snapshot
Path delta + reachability evidence
Operator value
Slow, noisy triage
Ranked, explainable alerts

## Slide 8
Solution Architecture and Design
RPKI
VALIDATOR
BGP
COLLECTOR
POLICY
PROFILE
EVENT NORMALIZER
STATE DIFF ENGINE
PATH GRAPH STORE
REACHABILITY ANALYZER
EXPLANATION API
Figure: System Architecture UML Diagram

## Slide 9
Data Flow Diagram
RPKI FEED
BGP FEED
1.0
NORMALIZE
2.0
CORRELATE
3.0
ASSESS
OPERATOR
D1 · STATE STORE
D2 · PATH INDEX
Figure: Data Flow Diagram (DFD)

## Slide 10
Deployment Timeline
Milestones remain editable; replace date placeholders after sprint planning.
Scope + datasets
[DATE]
Ingestion + diff
[DATE]
Graph + analysis
[DATE]
API + UI
[DATE]
Validate + demo
[DATE]

## Slide 11
Bibliography
[1] Lepinski, M.; Kent, S. RFC 6480: An Infrastructure to Support Secure Internet Routing. IETF, 2012.
[2] Mohapatra, P. et al. RFC 6811: BGP Prefix Origin Validation; updated operational guidance in RFC 8893. IETF, 2013 / 2020.
[3] Lepinski, M.; Sriram, K. RFC 8205: BGPsec Protocol Specification. IETF, 2017.
[4] Bush, R. RFC 8416: Simplified Local Internet Number Resource Management with the RPKI. IETF, 2018.
[5] Gilad, Y. et al. MaxLength Considered Harmful to the RPKI. CoNEXT, 2017.
Verify each reference before submission.

## Slide 12
Thank You for
Your Attention!
TEAM DEBUGS · AIORI HACKATHON 3 · PS-032
Make every RPKI change explainable — from authorization to path to reachability.
QUESTIONS